- A ship travels 50 km on a bearing of, then travels on a bearing of  for 140 km.  Find the distance traveled from the starting point to the ending point. ANS: 148.66 km

- Mark notices that the bearing of a tree on the opposite bank of a river flowing north is.  Lisa is on the same bank as Mark, but 428.3 meters away.  She notices that the bearing of the tree is .  The two banks are parallel.  What is the distance across the river? ANS: 293.4 3m

- A ship is sailing due north.  At a certain point the bearing of a lighthouse 12.5 km distant is NE.  Later on, the captain notices that the bearing of the lighthouse has become SE.  How far did the ship travel between the two observations of the lighthouse? ANS: 17.80 km

- Two ships leave a harbor together, traveling on courses that have an angle of between them.  They each travel 402 miles, how far apart are they?

ANS: 744.58 mi

- Airports A and B are 450 km apart, on an east-west line.  Tom flies in an approximately northeast direction from A to airport C.  From C, he flies 359 km on a bearing of to B.  How far is C from A? And on what bearing?

ANS: 281.26 km; or

- A ship leaves its home port and sails on a bearing of NE.  Another ship leaves the same port at the same time and sails on a bearing of SE.  If the first ship sails at 24 mph and the second ship sails at 28 mph, find the distance between the two ships after 4 hours. ANS: 147.51 mi

- A ship sailing parallel to shore sights a lighthouse at an angle of from its direction of travel.  After the ship travels 2 miles farther, the angle has increased to.  At that time, how far is the ship from the lighthouse? ANS: 2.37 mi

- A ship travels 70 km on a bearing of  and then travels on a bearing of for 180 km.  Find the distance of the end of the trip from the starting point.  ANS: 157.16 km

- Two lighthouses are located on a north-south line.  From lighthouse A the bearing of a ship 3742 m away is .  From lighthouse B the bearing of the ship is .  Find the distance between the lighthouses. ANS: 5856.1 0m

- Radio direction finders are set up at points A and B, which are 2.00 mi. apart on an east-west line.  From A it is found that the bearing of the signal from a radio transmitter is N E, while from B the bearing of the same signal is N W.  Find the distance of  the transmitter from B. ANS: 1.63 mi

- A plane flies at 300 miles per hour. There is a wind blowing out of the southeast at 86 miles per hour from a bearing of 140°. At what bearing must the plane head in order to have a true bearing of 14°? What will be the plane's groundspeed? ANS: 342.37 mph, 27.41°

- A plane traveling 500 mph in the direction 120° encounters a wind of 80 mph from a bearing of 225°. What is the resultant speed and direction of the plane? ANS: 526.41 mph, 111.56°

- A plane is headed due west with an air speed of 212 km/h. It is driven from its course by a wind from due north blowing at 23.6 km/h. Find ground speed of the plane and the actual direction of travel. ANS: 213.31 km/h, 263.65°.

- A plane flies with a heading of  N48°W and an air speed of 584 km/h. It is driven from its course by a wind of 58.0 km/h from S12.0°E. Find the ground speed and the resulting course of the plane. ANS:  631.84 km/h, N44.91W°

- Suppose that a wind is blowing from the direction N45°W at a speed of 40 km/h. A pilot is steering a plane in the direction N60°E at an airspeed of 200 km/h. Find the true course and the ground speed of the plane. ANS: 213.87, 70.41°

- In still air a plane has air speed 300km/h and flies on a bearing of 110°. If the wind is blowing at a speed of 100km/h from a bearing of 60°, find the actual velocity of the plane and the resulting course.  ANS: 247.86 km/h, 128°

- Pilot Megan McCarty’s flight plan has her leaving San Francisco International Airport and flying a Boeing 727 due east. There is a 65-mph wind blowing from a 240° bearing. Find the compass heading McCarty should follow, and determine what the airplane’s ground speed will be assuming that its speed with no wind is 450 mph. ANS: 505.12 mph, 94.14°

- A ship heads due south with the current flowing from a bearing of 135°. Two hours later the ship is 20 miles in the direction 30° west of south from the original starting point. Find the speed with no current of the ship and the rate of the current. ANS: 13.66 mph, 7.07 mph

- An airplane is flying on a bearing of 285° at 480 mph. A wind is blowing from a bearing of 85° at 30 mph. Find the actual speed and direction of the airplane.

ANS: 508.29 mph, 283.84°